## Slide 1: Manufacturing nitric acid

## Slide 2: Mainly fertilisers
Global production of nitric acid
Around 60,000,000 tonnes of nitric acid are produced annually.
However, it is difficult to obtain accurate figures. Much of it does not leave a production plant and is used to make fertilisers on site and does not reach the market. It has been estimated that only 10% of the total nitric acid made gets into the marketplace.
Uses
In 2010, nitric acid was used as follows:
80% used to make ammonium nitrate, of which nearly three-quarters are used in fertiliser applications.
2.5% used to make products such as nitrophosphates and potassium nitrates, also use in fertiliser applications.
10% used to make organic compounds such as nitrobenzene, toluene diisocyanate, adipic acid, and nitrochlorobenzenes.
7.5% of nitric acid is used in other non-fertiliser applications.
the use of ammonium nitrate as a fertiliser is declining because of concerns about nitrate groundwater contamination, the use of solid urea has increased.
toluene diisocyanate is used to make polyurethanes
adipic acid is used to make nylon.

## Slide 3: The process
Raw materials
Three raw materials are needed for the nitric acid process:
Ammonia
Air
Water
Nitric acid plant
A nitric acid plant has a number of key sections:
Ammonia evaporation
Ammonia converter
Absorption
Most nitric acid plants are situated close to an
ammonia production.

## Slide 4: Oxidation of ammonia
The chemistry
Ammonia is oxidised by oxygen in air to make nitrogen monoxide (common name: nitric oxide),
4NH3 + 5O2  4NO + 6H2O ∆Ho298 = −940 kJ mol−1
The reaction is catalysed by an alloy of platinum and rhodium.
Other reactions also occur such as
4NH3 + 3O2  2N2 + 6H2O ∆Ho298 = −11268 kJ mol−1
4NH3 + 4O2  2N2O + 6H2O ∆Ho298 = −1140 kJ mol−1
The yield of nitric oxide depends on pressure and temperature as indicated in the table.
These exothermic reactions release energy to produce steam and/or to preheat the waste gas. After this energy transfer, the temperature of the gas is 100 to 200 oC, depending on the process. It is cooled further with water.
Further air is mixed with the nitrogen monoxide to oxidise it to nitrogen dioxide
2NO + O2 ⇌ 2NO2 ∆Ho298 = −112 kJ mol−1
Nitrogen dioxide dimerises to dinitrogen tetraoxide
2NO2 ⇌ N2O4 ∆Ho298 = −57.2 kJ mol−1
The plant
Pressure (kPa) | Temperature (oC) | NO yield (%)
<170 | 810 - 850 | 97
170 to 650 | 850 - 900 | 96
>650 | 900 – 940 | 95

## Slide 5: Absorption
Dissolving oxides of nitrogen in water
The gas entering the absorption tower is a mixture of nitrogen dioxide and dinitrogen tetraoxide.
A counter-current flow of water is used to absorb the nitrogen dioxide. A number of reactions happen, but the overall reaction may be summarised by the equations:
4NO2 + 2H2O + O2  4HNO3
2N2O4 + 2H2O + O2  4HNO3
The contributing reactions include:
3NO2 + H2O ⇌ 2HNO3 + NO
N2O4 + H2O  HNO2 + HNO3
3HNO2  HNO3 + H2O + 2NO
A secondary air stream is introduced to re-oxidise NO and to remove move NO2 from the product acid.
Environmental improvements
Special reactors are included in most modern plant and refitted into older plant to reduce emissions of oxides of nitrogen. The reduction takes place over a catalyst, and the reaction may be summarised as:
6NO2 + 8NH3  7N2 + 12H2O