## Slide 1: Manufacturing ammonia

## Slide 2: Fertilisers and much more
Global production of ammonia
Uses
Year | Tonnes of ammonia
2005 | 148 000 000
2006 | 153 000 000
2007 | 159 000 000
2008 | 158 000 000
2009 | 158 000 000
2010 | 159 000 000
The annual production of ammonia remained fairly constant over the past six years or so. Although manufactured in countries around the world, in 2009 the four biggest producers and the quantities they produced are:
China 51 352 000 tonnes
(about ⅓ of the world’s production)
India 13 600 000 tonnes
Russia 12 678 000 tonnes
USA 9 355 000 tonnes
80% of ammonia produced is used in the manufacture of fertilisers.
20% is used for other purposes:
plastics ● synthetic ● fibres ● explosives ● dyes ● pharmaceuticals ● industrial refrigerant ● industrial and domestic cleaning agent.

## Slide 3: The process
Raw materials
The raw materials needed are air, natural gas (or other hydrocarbons) and steam.
Removal of sulfur from feedstock, e.g. natural gas,
involves these chemical reactions:
R-SH + H2  H2S + RH
H2S + ZnO  ZnS + H2O
Ammonia plant
An ammonia plant has a number of key sections:
Primary reformer
Secondary reformer
Carbon dioxide absorber
Ammonia convertor

## Slide 4: Primary reformer
The chemistry
After the removal of sulfur compounds, the gas is mixed with superheated steam and fed into a primary reformer.
The mixture is heated to 770 oC in the presence of a nickel catalyst and these reversible reactions occur:
CH4 + H2O ⇌ CO + 3H2 ∆Ho298 = +206 kJ mol−1
CO + H2O ⇌ CO2 + H2 ∆Ho298 = −41 kJ mol−1
Overall reaction:
CH4 + 2H2O ⇌ CO2 + 4H2 ∆Ho298 = +165 kJ mol−1
The overall reaction (methane and steam to carbon dioxide and hydrogen) is highly endothermic.
Therefore, maintaining a high reaction temperature moves the position of equilibrium to the right.
The mixture that emerges is called synthesis gas.
The plant

## Slide 5: Secondary reformer
The shift conversion happens in two stages:
High temperature shift (iron oxide/chromium oxide catalyst at about 400 oC) that lowers the carbon monoxide content from 12-15% to about 3%.
Low temperature shift (copper oxide/zinc oxide-based catalyst at about 200-220 oC) which lowers the carbon monoxide content further to about 0.2-0.4%.
Reforming
Only 30-40% of the hydrocarbon is reformed in the primary reformer because of the equilibrium reactions. The synthesis gas is cooled slightly to 735 oC, mixed with air and passed into the secondary reformer. Highly exothermic reactions happen such as:
CH4 + 2O2  2H2O + CO2 ∆Ho298 = −82 kJ mol−1
With the energy released and further heating a temperature of about 1000 oC is reached and up to 99% conversion to methane to hydrogen achieved.
Nitrogen (from the air) is used later in the synthesis of ammonia.
Shift conversion
Any remaining carbon monoxide in the gas mixture is converted to carbon dioxide in the shift section of the process:
CO + H2O ⇌ CO2 + H2 ∆Ho298 = −41 kJ mol−1

## Slide 6: Ammonia synthesis
Removal of water and carbon dioxide
The gas mixture now consists of mainly hydrogen, nitrogen, carbon dioxide and steam. Cooling the gas causes steam to condense and be removed as liquid water.
Carbon dioxide is removed by chemical or physical absorption. It is used for the manufacture of urea.
Methanation
Any remaining amounts of carbon monoxide and carbon dioxide must be removed before the ammonia synthesis stage as they would poison the catalyst. This is done by reacting them with hydrogen at 300 oC over a nickel-containing catalyst.
CO + 3H2 ⇌ CH4 + H2O ∆Ho298 = −206 kJ mol−1
CO2 + 4H2 ⇌ CH4 + 2H2O ∆Ho298 = −165 kJ mol−1
The emerging gas must be completely dry and so water produced in these reactions is removed by condensation.
Ammonia synthesis
The synthesis of ammonia takes place on an iron catalyst at pressures usually in the range 10-25 MPa and temperatures in the range 350-550 oC
N2 + 3H2 ⇌ 2NH3 ∆Ho298 = –92 kJ mol−1
The conditions used are a compromise between yield, speed and energy demands.