## Slide 1: Naproxen – Lecture 1
Project briefing and introduction to process chemistry
Nimesh Mistry, Sarah Naramore and George Burslem
University of Leeds

## Slide 2: Brief
You and your colleagues are a team of research and development chemists.
You work for the process development section of a pharmaceutical company.
Your teacher is your line manager.
Our company produces (S)-naproxen, a non-steroidal anti-inflammatory drug.
The (S)-enantiomer is active and (R) enantiomer is not.
Notes: Non-steriodal anti-inflamatories (NSAIDs) are mostly used as pain killers. Well known NSAIDs include ibuprofen and paracetamol

## Slide 3: Naproxen synthesis
Notes: Production of the S-enantiomer requires resolution of a racemic mixture.
Our current synthetic route produces both enantiomers and then separates them.
The (R)-enantiomer goes to waste: this is too inefficient.
You must develop a method that will recycle the undesired (R)-enantiomer of naproxen into the (S)-enantiomer.
This method will need to be carried out on a pilot plant.

## Slide 4: Course overview
Week | Session | Length | Descriptions
1 | Lecture 1 | 1 h | Introduction to the project. An introduction to the process chemistry examining the ways plant chemistry is different to lab chemistry
1 | Workshop 1 | 1 h | Adapting laboratory scale reactions to pilot plant scale using the principles from lecture 1.
2 | Lecture 2 | 1 h | Health and safety. Green chemistry considerations. Time and cost in process chemistry.
2 | Workshop 2 | 1 h | Adapting laboratory scale reactions to pilot plant scale using the principles from lectures 1 and 2.
3 – 6 | Laboratory work | Timetabled | Laboratory investigations to find the optimum conditions to recycle (R)-naproxen.
7 | Group presentation | 20 – 30 min | A group presentation to the manager and pilot plant team.
9 – 10 | Written report due |  | Deadline for written report describing the project work and giving full experimental details for the lab work you carried out.

## Slide 5: Assessment
Project results 30%
Laboratory report 40%
Group presentation 20%
Peer mark 10%
The key to good results is good team work, planning and communication
Notes:   Project results assessed on: Quality and quantity of results, practical skills, independence, teamwork, problem-solving, chemical understanding and application
  Lab report based on: Overall presentation, quality of the introduction, results and discussion, experimental, conclusion and self-reflection
  Presentation based on: Structure, timing, content, quality of slides, delivery and response to questions
  Peer mark based on: Level of participation and teamwork

## Slide 6: Meet Matt Tozer
Matt Tozer is an industrial chemist

## Slide 7: Process scale chemistry 1
Research labs
Small scale (10 mg – 10 g)
Make many different compounds
Yields are unoptimised
Expensive, inefficient or dangerous reagents can be used
Notes: Many different compounds are made in medicinal chemistry so that they can be tested. Synthetic routes are often designed so that lots of different final compounds can be made from a common intermediate. Routes designed this way are not necessarily optimal for making just one particular compound.

## Slide 8: Process scale chemistry 2
Chemical plants
Large scale (tonnes)
Only need to make one product
Yields are highly optimised
Processes must be safe, efficient and cost-effective
Efficient plant scale routes take a considerable amount of time and work to develop

## Slide 9: Everything changes on scale
Reactions can’t be done using giant round bottomed flasks, separating funnels and Buchner funnels.
Glass and porcelain are too fragile.
You can’t move reactors around.
Notes: Glass is physically not strong enough to hold more than 200 L
Large filters would crack with the weight of material and/or when heated or cooled
You can’t lift them up or pour things out of them

## Slide 10: Reaction vessels
Discovery scale
Process research scale
Plant scale

## Slide 11: Plant vessel
Continuous stirred tank reactor

## Slide 12: Addition of reagents
Liquids added by pump, or residual vacuum
Solids added through charge port
Adding solids can be dangerous for workers
  Powders could be inhaled
  Could be splashed by liquids in vessel
Specialist equipment needed to add air-sensitive or pyrophoric reagents

## Slide 13: Heating and cooling
Standard reactors: -15 – 140 °C
Specialised vessels available for very cold or very hot reactions
Heat transfer is slow – low surface area to volume ratio
Because cooling is slow, exothermic reactions can “run away”
Notes: Batch reactor vessels have a jacket through which heat transfer fluid is circulated
Transfer of heat is much slower when you are dealing with large volumes: the surface area to volume ratio is much lower.
This needs to be considered when planning costs, time-scales and safety.
If an exothermic reaction in a round bottomed flask begins to get too hot, it is easy to get an ice-bath and cool it down; with a 5000 L reactor it can’t be cooled down, the reaction will run away from you and you may end up with an explosion or serious accident

## Slide 14: Work-up and transfer 1
Lab scale
Dilute/quench by addition of water
Extract into organic solvent
Dry over MgSO4
Concentrate using rotary evaporator
Purify by recrystallisation

## Slide 15: Work-up and transfer 2
Plant scale
Dilute/quench by addition of water
Extract into organic solvent
Remove excess solvent by distillation
Transfer slurry of product directly to next synthetic step
Change solvent by distillation if necessary

## Slide 16: Aqueous work-up

## Slide 17: Purification
Purification is usually saved for the last step in a synthetic route
Reactions are optimised so that there are few impurities
Most purifications are carried out by crystallisation.
Filtration is carried out using specialist equipment and the product is dried in ovens
Column chromatography can’t be done: too much solvent and silica is too dangerous.
Distillation is possible for low MW oils.

## Slide 18: Questions and discussion
Think about the lab techniques you’ve used in teaching labs.
Which techniques would be easiest to use on a pilot plant?
Are there any you couldn’t use at all?
Discuss your ideas with the people next to you.

## Slide 19: Answers
Easy: stirring, filtering, extraction, reflux, reactions under nitrogen, recrystallisation
moderate: use of pyrophoric reagents and other particularly hazardous reagents, reactions at high pressure, cryogenic reactions
Hard/impossible: rotary evaporation, column chromatography
Any other suggestions?
Notes: The easy steps can be carried out using standard plant equipment. Moderate steps require specialist equipment, but big plants will have this equipment if it is needed. Evaporation to dryness can’t be done with such large volumes and removing the solid from the vessel would be impractical even if it were possible. Specialised column chomatography can be carried out on moderate scale, but most companies will go to extreme lengths to avoid it because the solvent costs are so large and handling large volumes of silica is so dangerous

## Slide 20: Example process development
Final step in the synthesis of blood pressure medication Amlodipine.
First time in pilot plant yield was unexpectedly low.
Distillation of MeNH2 drives equilibrium back to starting material.

## Slide 21: Improved route 1
Original pilot plant process
Addition of EtOH and MeNH2 to solution of intermediate 1
Stirred until reaction complete
Volume reduced by distillation
Reaction quenched by addition of water
Organic layers separated
Concentrated to an oil
Crystallisation and filtration
Notes: Often the simpler the better when it comes to large scale chemistry especially at the work-up stage

## Slide 22: Improved route 2
New process solves this problem – No EtOH
Add MeNH2 to concentrated solution of intermediate 1
Stirred until reaction complete
Filter off product
Crystallisation and filtration
Notes: Often the simpler the better when it comes to large scale chemistry especially at the work-up stage

## Slide 23: Summary 1
Large scale chemistry is carried out differently to lab chemistry
Different techniques are used
Reactions need to be planned in a lot more detail

## Slide 24: Summary 2
Before the workshop – read the hand-out.
In the workshop you will be discussing the course outline and learning objectives

## Slide 25: Copyright information
This resource “new name”, is a derivative of “Naproxen lecture 1” by The Royal Society of Chemistry used under CC-BY-NC-SA 4.0. “new name” is licensed under CC-BY-NC-SA 4.0 by “name of user”.