## Slide 1: Naproxen – Lecture 2
Safety and environmental concerns in process chemistry
Nimesh Mistry, Sarah Naramore and George Burslem
University of Leeds

## Slide 2: Risk assessment
Hazards scale too
Video – importance of safety on process scale
Notes: Every year the journal OPRD publishes an issue focusing on safety

## Slide 3: Hazards and risk
Hazards are features of the process that could cause harm if something went wrong:
  Flammability of solvents
  Toxicities of reagents
  Reaction exotherms
  Faulty equipment
  Operator error
The risk is determined by the likelihood that something will go wrong and the degree of harm it would cause

## Slide 4: Mitigating risks 1
Here are some examples of hazards and approaches to mitigating the risks associated with them.
Flammable solvents:
  Use a less flammable solvent
  Run the reaction at a lower temperature
  Check the condenser is working before each reaction

## Slide 5: Mitigating risks 2
Exothermic reactions:
  Understand the thermodynamics of the process
  Set safe operating temperatures and know what to do if the temperature begins to exceed the threshold
  Have a contingency plan in the event of a run-away reaction

## Slide 6: Worst case scenarios
Risk assessments should state clearly how to perform a procedure in a way that minimises the risks.
It should also explain what to do if something goes wrong:
  What if the cooling system fails
  What if a pipe starts leaking when adding solvent
  What if a worker inhales some of a reagent
Notes: The risks of these things happening is low, but the consequences would be very serious, so they need to be considered and the proceedures to be followed in the case of an emergency should be understood by everyone.

## Slide 7: Route design to minimise hazards 1
This hydrazine condensation reaction has some serious hazards:
  Hydrazine is toxic and highly flammable
  Reaction is exothermic
  Reaction produces HCl
  Intermediate can react with HCl and then decompose exothermically at 70 °C
Notes: Recently published in OPRD. The exothermic decomposition is the key hazard. If the reactive intermediate isn’t formed the threshold for a dangerous exotherm was >200 °C and so they could rely on evaporation of solvent preventing the temperature getting that high in the event of a coolant failure. 70 °C is too low for evaporation of solvent to protect the reaction if the cooling failed.

## Slide 8: Route design to minimise hazards 2
A thorough process safety review was conducted
Adding base to the reaction was shown to prevent exotherm below 300 °C
Many solvents and bases were screened to find the best combination: pyridine and sodium acetate
Reaction proceeds quickly, so exposure of workers to hydrazine is minimised
Notes: The base neutralises the HCl given off by the reaction, so the unstable intermediate isn’t formed and there is no danger of an uncontrollable exotherm even if the cooling does fail, because evaporation of the solvent will cool the reaction enough for it to stay safe until the reaction is over.

## Slide 9: Question and discussion
There are risks involved in everyday activities too, but you are aware of the risks and minimise them without having to think about it.
Make a list of the hazards involved in crossing the road and making a cup of tea. What actions do you take to minimise these risks?
Discuss with the people next to you.
Notes: This discussion shouldn’t take more than a few minutes.

## Slide 10: Answers 1
Making tea
Hot water could cause burns: pour carefully and avoid skin contact. If you burn yourself then use whatever first aid is appropriate.
Kettle could catch fire: look out for damage to the kettle, always fill above minimum water level. If kettle catches fire turn of the electricity and follow normal fire fighting procedures.
Milk could be off: check milk before use. If not tea tastes sour, remake with fresh milk.

## Slide 11: Answers 2
Crossing the road
Could be hit by a car: look both ways, listen for engines, use pedestrian crossing if available. If an accident does occur, call for help and dial 999.

## Slide 12: Green chemistry 1
Environmental impact of reactions must be considered in advance for several reasons:
Ethical:
  Accidental leakage of chemical waste can cause serious harm
  Health of workers and the general public
  Energy usage contributes to global warming
  Chemical precursors often come from fossil fuels

## Slide 13: Green chemistry 2
Financial:
  Disposal of hazardous waste is expensive
  Energy costs of a process can be considerable
Legal:
  strict laws in place to protect the environment

## Slide 14: Key considerations
Reactions should be carried out efficiently
Chlorinated solvents should be avoided
Energy usage should be minimised
Use renewably sourced materials where possible
Synthetic routes should be as simple as possible
Catalysis should be used wherever possible
Reagents with severe hazards should be avoided
Notes: Solvents like DCM are strictly controlled as they can cause damage to the atmosphere. Their use is heavily restricted and their disposal is very expensive. Much better to find an alternative solvent if possible
Better to do a reaction at a low temperature for a longer time that short time at a higher temperature, unless the reaction will produce unwanted side products that might add extra steps to the work-up
The more hazardous a reagent the more expensive/ time consuming it will be to dispose of and the greater the damage to people and the environment if there was to be a leak or accident

## Slide 15: Discussion and questions
Below are two different procedures for carrying out an amide coupling. Which is greener and why?
Notes: HOBt = hydroxybenzotriazole explosive when dry, so kept as a HOBt.H2O
EDC = 1-Ethyl-3-(3-dimethylaminopropyl)carbodiimide
DMF = dimethyl formamide
T3P = propylphosphonic anhydride is technically classed as a schedule 2 chemical weapons precursor based on its chemical structure (no one’s ever actually used it to make a chemical weapon), so a bit of extra paperwork is needed to use it, but industry is usually pretty happy to do the paperwork because it’s so much greener than alternative amide coupling reagents
EtOAc ethyl acetate

## Slide 16: Answers
The second route is greener.
T3P is less hazardous than HOBt and EDC
Ethyl acetate is a greener solvent than DMF
Second route is higher yielding
Better to recrystallise than column

## Slide 17: Costs 1
2 categories
Variable costs – change depending on the reactions you are carrying out:
  Costs of raw materials
  Heating and cooling of reaction vessels
  Disposal of waste

## Slide 18: Costs 2
Fixed costs – don’t depend on which reactions are being carried out:
  Building maintenance
  Wages for plant workers
  Insurance

## Slide 19: Summary 1
Risk assessment is critical on large scale
The environmental impact of processes must be considered
The costs of different synthetic routes must be considered

## Slide 20: Summary 2
Before the workshop – Read about the steps you will have to optimise.
In the workshop you will be discussing different reaction conditions

## Slide 21: Copyright information
This resource “new name”, is a derivative of “Naproxen lecture 2” by The Royal Society of Chemistry used under CC-BY-NC-SA 4.0. “new name” is licensed under CC-BY-NC-SA 4.0 by “name of user”.