## Slide 1: Nuclear decommissioning: Turning waste into Wealth
Disposal of low-level radiation
Tzany Kokalova
University of Birmingham

## Slide 2: Overview
Aims
Classification of radioactive waste
Current methods of disposal for each waste type
The UK low-level radioactive waste facility
Low-level radioactive waste storage

## Slide 3: Radioactive waste 1
Categories of radioactive waste are based on precise classifications:
low-level
intermediate-level
high-level

## Slide 4: Radioactive waste 2
How do you think the following wastes should be categorised?
Molten reprocessing waste (actinides etc.)
Contaminated gloves and show covers
Metal cladding from the reactor
Notes: Ask the students how they would categorise waste given the task.

## Slide 5: Examples of waste 1
Low-level waste
Contaminated protective shoe covers
Clothing
Wiping rags
Mops
Filters
Reactor water treatment residues
Smoke detectors
From hospitals and industry, as well as reactor sites

## Slide 6: Examples of waste 2
Intermediate-level waste
Metal cladding
Moderator from a reactor upon decommissioning

## Slide 7: Examples of waste 3
High-level waste
Waste left over after reprocessing spent fuel. Needs cooling as the radioactivity generated heat.
Low-level waste accounts for >90% of the overall waste volume but about 0.1% of the radioactivity.
(Source: nda.gov.uk, 2015)
Notes: Discuss spent fuel.
UK policy differs from that of other countries, e.g. the USA. In the UK, the spent fuel itself is classed as an asset, not waste.
Ask for advantages and disadvantages for this policy. E.g. reprocessing costs and complexity, but retrieval of usable fuel.

## Slide 8: Categories of waste 1
Low-level waste
Waste for which the radioactive content does not exceed 4 GBq/Tonne of α or 12 GBq/Tonne of β-γ activity.
Does not require shielding during handling/transport
Source: Disposal of radioactive waste - http://bit.ly/1U5hDMS
Notes: Reminder of alpha, beta and gamma radiation, via asking the students to contribute aspects of each decay, e.g. particles emitted energy released (Q-value) and majority energy carriers.
Link to smoke detectors – Am-241 is an alpha emitter. Smoke detectors would be low-level waste.

## Slide 9: Categories of waste 2
Intermediate-level waste
Waste with higher levels of radioactivity than low-level waste, but not significantly heat-generating
Source: Disposal of radioactive waste - http://bit.ly/1U5hDMS
Notes: Reminder of alpha, beta and gamma radiation, via asking the students to contribute aspects of each decay, e.g. particles emitted energy released (Q-value) and majority energy carriers.
Link to smoke detectors – Am-241 is an alpha emitter. Smoke detectors would be low-level waste.

## Slide 10: Categories of waste 3
High-level waste
Waste with higher levels of radioactivity than low-level waste, but for which the decay heat is significant enough to raise its temperature and that of the surroundings. Cooling needs to be taken into account when handling and storing.
Source: Disposal of radioactive waste - http://bit.ly/1U5hDMS
Notes: Reminder of alpha, beta and gamma radiation, via asking the students to contribute aspects of each decay, e.g. particles emitted energy released (Q-value) and majority energy carriers.
Link to smoke detectors – Am-241 is an alpha emitter. Smoke detectors would be low-level waste.

## Slide 11: Treatment of waste in the UK 1
Low-level waste
Compacted and encased in concrete
Stored near ground level, e.g. at the UK’s low-level waste repository
Notes: Discussion of strategies and the logic behind them.
Appreciation of the bulk of low-level waste that would quickly fill any geological disposal repository, so it is not intended for such a facility.
High-level waste surface storage enables monitoring of the temperature, integrity and activity of the waste.
Intermediate level waste is awaiting a long-term storage facility in the UK. Discuss why?
Social issues, community don't want it on their door step. Ground-water contamination fear.
Strategy to decide, should the waste be retrievable.

## Slide 12: Treatment of waste in the UK 2
Intermediate-level waste
Encased in cement inside concrete boxes or steel drums.
Stored at sites awaiting future long term solution, e.g. geological storage (GDF)
Notes: Discussion of strategies and the logic behind them.
Appreciation of the bulk of low-level waste that would quickly fill any geological disposal repository, so it is not intended for such a facility.
High-level waste surface storage enables monitoring of the temperature, integrity and activity of the waste.
Intermediate level waste is awaiting a long-term storage facility in the UK. Discuss why?
Social issues, community don't want it on their door step. Ground-water contamination fear.
Strategy to decide, should the waste be retrievable.

## Slide 13: Treatment of waste in the UK 3
High-level waste
Vitrified – transformed into borosilicate glass (pyrex) inside robust stainless steel containers. These are welded closed and stored at the surface for a minimum of 50 years, then to GDF.
Notes: Discussion of strategies and the logic behind them.
Appreciation of the bulk of low-level waste that would quickly fill any geological disposal repository, so it is not intended for such a facility.
High-level waste surface storage enables monitoring of the temperature, integrity and activity of the waste.
Intermediate level waste is awaiting a long-term storage facility in the UK. Discuss why?
Social issues, community don't want it on their door step. Ground-water contamination fear.
Strategy to decide, should the waste be retrievable.

## Slide 14: The low-level waste repository 1
LLWR
Established in 1959 at Drigg, West Cumbria.
Owned by UK Nuclear Waste Management Ltd.

## Slide 15: The Low-level waste repository 2

## Slide 16: Low-level waste procedures 1
Compaction and grouting
The large volume of low-level waste mean compaction or super-compaction (if machines using ~1000 Tonnes pressure) are used.
Grouting (encased in cement).
Stacked in a near-surface vault.
Notes: Discuss alternatives to storage. E.g. incineration.
For high-level waste the equivalent would be and accelerator driven system (ADS). Introduce. the EUs MYRRHA project in Belgium – energy from radioactive waste.

## Slide 17: Low-level waste procedures 2
Surface discharge by nuclear reactor operators
Gases and liquids to the air or sea
Governed by UK environmental agency permits
Notes: Discuss alternatives to storage. E.g. incineration.
For high-level waste the equivalent would be and accelerator driven system (ADS). Introduce. the EUs MYRRHA project in Belgium – energy from radioactive waste.

## Slide 18: Objectives
After this workshop you should be able to:
Classify radioactive waste into the appropriate category based on waste properties
Articulate current UK radioactive waste strategies for each category
Justify the strategies based on radioactivity and volumes
Appreciate differences in how fuel is treated internationally, especially spent reactor fuel.

## Slide 19: Bibliography 1
Sources/further reading
Office of Nuclear Regulation (ONR) (governmental body).
http://www.onr.org.uk/
EDF Energy, operator of the UKs current nuclear reactors.
http://www.edfenergy.com/
Low-level waste repository Ltd.
http://llwrsite.com/

## Slide 20: Bibliography 2
Sources/further reading
Dounreay. A nuclear site undergoing decommissioning.
http://www.dounreay.com/
World Nuclear Association: an organisation for the nuclear profession.
http://www.world-nuclear.org/

## Slide 21: Copyright information
This resource “new name”, is a derivative of “W2W Low level disposal” by The Royal Society of Chemistry used under CC-BY-NC-SA 4.0. “new name” is licensed under CC-BY-NC-SA 4.0 by “name of user”.