## Slide 1: Nuclear decommissioning: Turning waste into Wealth
Radiochemistry and the nuclear fuel cycle
Tzany Kokalova
University of Birmingham

## Slide 2: Overview
Aims
Introduction to radiochemistry techniques
Key radionuclide chemistry
Stages of the nuclear fuel cycle
Hazards and wastes arising from the fuel cycle
Basic chemistry of the processing stages

## Slide 3: Radiochemistry techniques 1
Radiochemical separations
Precipitation
Solvent extraction
Ion-exchange chromatography
Extraction chromatography

## Slide 4: Radiochemistry techniques 2
Precipitation
Precipitation involves the creation of a solid during a chemical reaction.
This could be in solution or within another solid

## Slide 5: Radiochemistry techniques 3
Solvent extraction
Actinides (U/Pu) form complexes with tri-butyl phosphate (TBP) in kerosene, other contaminants do not. E.g.
Pu4+ + 4NO3- + 2TBP ⇌ Pu(NO3)4.2TBP
Pu can be extracted with the solvent.

## Slide 6: Radiochemistry 1
Ion-exchange chromatography
Ion-exchange chromatography allows the separation of ions and polar molecules.
Molecules with +ve charge on one side and -ve on the other – based on their affinity to the ion exchanger.
Can be used for a wide range of charged molecules.

## Slide 7: Radiochemistry 2
Extraction chromatography
The separation is based on the distribution of radionuclides between organic and aqueous phases.
A wide variety of extractants: acidic, amines, organic molecules etc.

## Slide 8: Key technique: Solvent extraction 1
Advantages
Rapid, highly efficient and very selective separations.
Partition coefficients independent of radionuclide concentration.
Can usually be followed by back-extraction into aqueous solutions.
Notes: Solvent extract is used both in the processing of yellowcake into uranium fuel and in the reprocessing of spent fuel, in order to separate Pu and U the fission products and other actinides. This is covered in later slides on reprocessing.

## Slide 9: Key technique: Solvent extraction 2
Advantages
Wide scope of applications – the composition of the organic phase and the nature of complexing or binding agents can be varied so that the number of practical combinations is virtually unlimited.
Can be performed with simple equipment, but can also be automated.
Notes: Solvent extract is used both in the processing of yellowcake into uranium fuel and in the reprocessing of spent fuel, in order to separate Pu and U the fission products and other actinides. This is covered in later slides on reprocessing.

## Slide 10: Key technique: Solvent extraction 3
Disadvantages
Often requires toxic or flammable solvents
Time consuming, especially if the equilibrium is slow.
Can require costly amounts of organic solvents and generate
Large volumes of organic waste.
Can be affected by small impurities in the solvent.
Multiple extractions might be required, thereby increasing time, consumption of materials, and generation of waste.
Notes: Solvent extract is used both in the processing of yellowcake into uranium fuel and in the reprocessing of spent fuel, in order to separate Pu and U the fission products and other actinides. This is covered in later slides on reprocessing.

## Slide 11: Tracers and carriers 1
Carriers
Carriers are chemically identical materials to the radionuclide of interest that have a significant, non-radioactive mass. By adding such a material to the radionuclide of interest the carrier, rather than the radionuclide can saturate loss-sites such as surfaces.
Examples
For 90Sr the stable isotope 88Sr can be used as a carrier.
Radium has no stable isotopes, but barium is in the same chemical group (II) can be used. Both will precipitate together.
Notes: A related point is that when so called 'pure' materials undergo neutron activation, e.g. in a reactor, this often reveals small quantities of contaminants which are other elements in the same chemical group.
Strontium-90 is a nuclear fission product with a half-life of 28.8 years and present in significant amounts in spent fuel.

## Slide 12: Tracers and carriers 2
Tracers
Tracers must exhibit the same chemical behaviour as the analyte – substance of interest – so that the same separations etc. can be performed. The tracer is added in a known quantity and measured at the end, enabling the losses of the processes to be found.
Example
Uranium-236 and 232 are used as tracers for 238U and 234U.
Notes: A related point is that when so called 'pure' materials undergo neutron activation, e.g. in a reactor, this often reveals small quantities of contaminants which are other elements in the same chemical group.
Strontium-90 is a nuclear fission product with a half-life of 28.8 years and present in significant amounts in spent fuel.

## Slide 13: Key radionuclides 1
Ion-exchange separation of actinides:
Am(III)
Pu(IV)
Np(V)
U(VI).
Notes: Remind students that the Roman numeral notation refers to the particular oxidation state (i.e. oxide).
Also a reminder that elution is the extraction using a solvent.
These separations are still and active area of research as different nuclides become of interest due to different applications and challenges, e.g. decommissioning.

## Slide 14: Key radionuclides 2
Actinides
8 M HNO3 + 0.1 M NaNO2
Anion-exchange resin AG1 fixes Pu & Np
8 M HNO3 + 0.1 M NaNO2
+ 9 M HCl
Anion exchange resin AG1 fixes U
Redox agent (NaNO2) stabilises Pu as Pu(IV) and Np as Np(V)
Np eluted by 2 M HCl
Np
Pu(III) eluted by:
9 M HCl + 0.1 M NH4I
Pu(III)
U eluted by:
1 M HCl
U
Am rinsed out
Am
Remainder material from 1st exchanger is passed to the 2nd
Notes: Remind students that the Roman numeral notation refers to the particular oxidation state (i.e. oxide).
Also a reminder that elution is the extraction using a solvent.
These separations are still and active area of research as different nuclides become of interest due to different applications and challenges, e.g. decommissioning.

## Slide 15: What is the nuclear fuel cycle? 1
The fuel cycle is a chain of industrial processes to convert the uranium ore into fuel for reactors and, following removal from the core, can also include the steps required to reprocess the spent fuel.
Notes: Remind students of the key facts about uranium
i.e. the natural abundances and half-lives:
Natural uranium has 3 isotopes:
Isotope Abundance Half-life
234U 0.0054% 2.46x105 years
235U 0.7204% 7.04x108 years
238U 99.2724% 4.47x109 years
and how these are linked, i.e. short lifetimes, more has decayed, so less remaining → lower abundance observed today.
As an aside, looking at these abundance ratios tells us the age of the earth.

## Slide 16: What is the nuclear fuel cycle? 2
Uranium
Uranium is a relatively common element found in the earth's crust. Before uranium can be used as fuel in reactors it must be converted from its natural forms.
Notes: Remind students of the key facts about uranium
i.e. the natural abundances and half-lives:
Natural uranium has 3 isotopes:
Isotope Abundance Half-life
234U 0.0054% 2.46x105 years
235U 0.7204% 7.04x108 years
238U 99.2724% 4.47x109 years
and how these are linked, i.e. short lifetimes, more has decayed, so less remaining → lower abundance observed today.
As an aside, looking at these abundance ratios tells us the age of the earth.

## Slide 17: What is the nuclear fuel cycle? 3
Uranium ore
Uranium ore consists of impure UO2, UO3, U3O8 and other material (contaminants).
Notes: Remind students of the key facts about uranium
i.e. the natural abundances and half-lives:
Natural uranium has 3 isotopes:
Isotope Abundance Half-life
234U 0.0054% 2.46x105 years
235U 0.7204% 7.04x108 years
238U 99.2724% 4.47x109 years
and how these are linked, i.e. short lifetimes, more has decayed, so less remaining → lower abundance observed today.
As an aside, looking at these abundance ratios tells us the age of the earth.

## Slide 18: What is the nuclear fuel cycle? 4
Radioactivity
Much of the radioactivity present with uranium deposits is from the decay products (daughter nuclei) e.g. radon gas, which are removed in the processing.
Notes: Remind students of the key facts about uranium
i.e. the natural abundances and half-lives:
Natural uranium has 3 isotopes:
Isotope Abundance Half-life
234U 0.0054% 2.46x105 years
235U 0.7204% 7.04x108 years
238U 99.2724% 4.47x109 years
and how these are linked, i.e. short lifetimes, more has decayed, so less remaining → lower abundance observed today.
As an aside, looking at these abundance ratios tells us the age of the earth.

## Slide 19: Overview of the fuel cycle
Mining and
milling
Tailings
Conversion
UF6 production
Natural U fuel
Enrichment
3.5 – 5% 235U
Fuel fabrication
Power plant
(electricity production)
High-level
waste storage
Disposal
Reprocessing
of spent fuel
Recycling
Notes: Discuss the various steps in the chain.
Tailings should be mentioned at the point. These are the leftovers from milling, i.e. mostly non-uranium containing rocks and minerals, but it is these that contain most of the radioactivity. They are typically placed in a specially engineered facility or pit near the mine.

## Slide 20: Key steps in the fuel cycle 1
Mining
The ore is extracted by either excavation or in situ leaching (ISL) with oxygenated water. Depending on conditions of the ore, weak acid or alkali solutions may be used in leaching.

## Slide 21: Key steps in the fuel cycle 2
Milling
Milling is generally performed close to the mine. This refers to the process of producing yellowcake. The ore is crushed and purified to extract U3O8 triuranium octoxide also known as yellowcake. See handout 'The chemistry of cake' for details.

## Slide 22: Key steps in the fuel cycle 3
Conversion
Conversion refinement to UO2 uranium dioxide. This can be used directly as a natural fuel for reactors needing no enrichment (0.7% 235U), or converted to UF6 uranium hexafluoride gas for enrichment.

## Slide 23: Key steps in the fuel cycle 4
Enrichment
Enrichment is the process by which the % of 235U is increased. The UF6 is allowed to solidify (melting point 64 °C) in metal containers for transport to the enrichment facility. Gaseous diffusion or centrifuges are used to perform the enrichment.

## Slide 24: Key steps in the fuel cycle 5
Fuel fabrication
Fuel for most reactor types is in ceramic pellets formed by pressed UO2 held at high temperatures. Lots of pellets are typically placed into tubes – fuel rods – which are combined together into groups, called stringers, ready to be placed into the reactor.

## Slide 25: Key steps in the fuel cycle 6
Reprocessing
Reprocessing is the process by which fissile material (e.g. Pu) is separated out from the fission products. This material can be used as new reactor fuel.

## Slide 26: Key steps in the fuel cycle 7
Storage
High-level waste requires cooling to remove the heat generated by radioactive decay. This waste is stored near the surface for at least 50 years in order to enable monitoring.
Site in Utah constructed for uranium mill tailings and debris from a mill site.

## Slide 27: Wastes and hazards 1
Tailings
These wastes from the mining process are not classified as radioactive waste, as they originated from naturally occurring ores and generally retained near the mine site.

## Slide 28: Wastes and hazards 2
Low-level waste
Produced from all stages in the fuel cycle
Intermediate-level waste
Largely produced from reactor operation and processing
High-level waste
Produced in the form of actinide nuclei and fission products separated from the fuel during reprocessing

## Slide 29: Depleted uranium (DU)
Depleted uranium (DU) is a by-product of the enrichment process. It refers to predominantly 238U in which the % of 235U is less than 0.7% – the uranium is thus depleted in 235U. Due to its high density, depleted uranium has applications in shielding and trim weights in aircraft as well as military uses. Thus, not all DU is waste.

## Slide 30: Chemistry of conversion 1
Dry process
The triuranium octoxide is heated to drive off impurities, then collected together and crushed. This is known as the dry process.
U3O8 + 2H2 → 3UO2 + 2H2O
The oxide is reduced in a kiln with hydrogen gas.

## Slide 31: Chemistry of conversion 2
Wet process
Involves:
Dissolving U3O8 in nitric acid to form uranyl nitrate UO2(NO3)2.6H2O.
Fed into a solvent extraction process using tributyl phosphate dissolved in kerosene or dodecane (long-chain hydrocarbons used as organic solvents).

## Slide 32: Chemistry of conversion 3
Wet process
Involves:
The uranium is collected and washed out of the solvent.
The product is concentrated by evaporation.
The solution is heated yielding UO3 or UO2 (under extreme heating).
UO3 + H2 → UO2 + H2O (Again, a reduction using hydrogen)

## Slide 33: Chemistry of conversion 4
Production of uranium hexafluoride
Step 1
Uranium dioxide heated in kiln with HF
UO2 + 4HF → UF4 + 2H2O
Occasionally, HF is reacted in aqueous solution (wet process)
Notes: Here one of the possible processes is given. Direct vaporisation of UO2 in a high temperature flame is possible: UO2 + 3F2 → UF6 (gas)

## Slide 34: Chemistry of conversion 5
Production of uranium hexafluoride
Step 2
Finally, UF4 reacted with F2(g) in a fluidised bed (flame tower) at 800 – 1200 °C
UF4 + F2  UF6
The UF6 is condensed in thick-walled steel shipping containers, as a white crystalline solid.
Notes: Here one of the possible processes is given. Direct vaporisation of UO2 in a high temperature flame is possible: UO2 + 3F2 → UF6 (gas)

## Slide 35: The PUREX process 1
PUREX – Plutonium Uranium Redox Extraction process
Same solvent extraction process as wet process for producing UO2
Specifically, PUREX refers to the process used in reprocessing.
Aim of reprocessing: To extract U and Pu from spent fuel.
When combined these form what is known as MOX – mixed oxide fuel.
Notes: The advantages and disadvantages of reprocessing could be discussed:
reduced amount of wasted fuel – less mining.
Similar waste volumes to purification of original uranium and no enrichment required.
Disadvantages are possible proliferation issues due to plutonium extraction, also large industrial scale facilities are required and the spent fuel being handled is highly radioactive.

## Slide 36: The PUREX process 2
Separation
In the solvent extraction the Pu and U are separated from fission products, which remain in the aqueous phase.
Transuranium elements americium and curium also remain in the aqueous phase rather than forming complexes with nitrate etc.
Notes: The advantages and disadvantages of reprocessing could be discussed:
reduced amount of wasted fuel – less mining.
Similar waste volumes to purification of original uranium and no enrichment required.
Disadvantages are possible proliferation issues due to plutonium extraction, also large industrial scale facilities are required and the spent fuel being handled is highly radioactive.

## Slide 37: Objectives
After this workshop you should be able to:
Describe the principles behind radiochemical separation
Appraise the technique of solvent extraction
Draw the separation method used for actinides/radionuclides
Sequence the key steps in the nuclear fuel cycle
Explain chemical process used in conversion and reprocessing.

## Slide 38: Bibliography 1
Sources/further reading
World Nuclear Association: an organisation for the nuclear profession.
http://www.world-nuclear.org/
International Atomic Energy Agency
https://www.iaea.org/

## Slide 39: Bibliography 2
Sources/further reading
Gregory Choppin, Jan-Olov Liljenzin and Jan Rydberg,
Radiochemistry and Nuclear Chemistry, Third Edition (2001).
Gerhart Friedlander and Joseph W. Kennedy,
Introduction to Radiochemistry, (John Wiley and Sons,1949).

## Slide 40: Copyright information
This resource “new name”, is a derivative of “W2W Radiochemistry” by The Royal Society of Chemistry used under CC-BY-NC-SA 4.0. “new name” is licensed under CC-BY-NC-SA 4.0 by “name of user”.