## Slide 1: Cheaper lithium extraction
Extracting lithium is unsustainable. Lithium is extracted by electrolysing a molten mixture of lithium chloride and potassium chloride. The source of lithium chloride is underground salt water. The salt water also contains other metal ions such as sodium and aluminium, which must be separated from the lithium chloride. The purification process uses noxious chemicals.
Read the full article at rsc.li/2VNT6Cl
Now, scientists have found that adding a layer of a solid ceramic into the electrolysis cell makes the process more sustainable. Only lithium ions can pass through the ceramic, so the cell can use unpurified lithium chloride. The impurities are left behind in the molten salt. The scientists could also add aluminium chloride to the molten salt to lower the melting point of the electrolyte.
Lithium thionyl chloride batteries
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson on electrolysis of molten salts.
Image みはりん / CC BY-SA (https://creativecommons.org/licenses/by-sa/3.0)

## Slide 2: Cheaper lithium extraction
Extracting lithium is unsustainable. Lithium is extracted by electrolysing a molten mixture of lithium chloride and potassium chloride. The source of lithium chloride is underground salt water. The salt water also contains other metal ions such as sodium and aluminium, which must be separated from the lithium chloride. The purification process uses noxious chemicals.
Read the full article at rsc.li/2VNT6Cl
Now scientists have found that adding a layer of a solid ceramic into the electrolysis cell makes the process more sustainable. Only lithium ions can pass through the ceramic, so the cell can use unpurified lithium chloride. The impurities are left behind in the molten salt. The scientists could also add aluminium chloride to the molten salt to lower the melting point of the electrolyte.
Explain why the electrolyte mixture has to be molten.
Explain why lithium forms at the negative electrode in electrolysis.
Explain why adding aluminium chloride makes the process cheaper.
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson on electrolysis of molten salts.
Answers
So the ions are free to move to the electrodes.
The lithium ions are positive and are attracted to the negative electrode.
Aluminium chloride lowers the melting point which means less energy is used to heat the electrolyte.