## Slide 1
Discounted Cash Flow
Topics Covered
Time Value of Money
Net Present Value (NPV)
Discounted Cash Flow (DCF)
Internal Rate of Return (IRR)
DiscountCashFlow | 1
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 2
Time Value of Money
Cash flows are discounted to take into account the fact that £1 000 to be received some time in the future is worth less today than £1 000 received immediately.
Why? Cash-in-hand is certain therefore less risky
Opportunities to invest cash today to earn interest
Let A = sum of money today
r = annual rate of return (as decimal)
B1 = sum of money after one year
B1 = A + A × r
B1 = A ( 1 + r )
DiscountCashFlow | 2
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 3
Time Value of Money
Let B2 = sum of money after 2 years
B2 = B1 + B1 r = A (1 + r ) + A (1 + r ) r
B2 = A (1 + r ) (1 + r )
In general: Bt = A ( 1 + r )t the compound interest formula
Points to note: “t” can be any positive number and “r” can be quoted for any period provided “t” is measured in the same units
Example
A credit card charges 2% per month for outstanding balances.
What is the interest rate being charged per annum ?
( 1 + 0.02 )12 = 1.268 or 26.8 %
DiscountCashFlow | 3
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 4
Time Value of Money
Will “B” always be greater than “A” ?
Switzerland (1970's) and Hong Kong (1990's) imposed negative interest rates to deter speculators - what would be the problems?
Normally governments increase interest rates to stop speculators selling currency.
Can calculate the present value (PV) if we know B , r and t .
Can calculate the future value (FV) if we know A , r and t .
Investment appraisal requires the present value so the discounting formula becomes:
Present value = Future value
( 1 + r )t
DiscountCashFlow | 4
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 5
Net Present Value (NPV)
You have won £150 000 on the national lottery.
Option 1: Buy a piece of land which you know you could sell for £250 000 in a years time.
Option 2: Buy Government gilt-edged securities which offer a 10% per annum return.
Present Value of Option 2 = £150 000
Present Value of Option 1 = Future value = £250 000
( 1 + r ) t ( 1 + 0.1)1
= £227 237
(the amount you would need to invest today )
DiscountCashFlow | 5
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 6
Net Present Value
Net Present Value for land purchase
= £227 237 - £150 000
= £77 273
The Investment Decision is:
If NPV is positive - accept the project
If NPV is negative - reject the project
And accept the project with the highest NPV
Therefore choose Option 1: Buy the land.
DiscountCashFlow | 6
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 7
Discounted Cash Flow (DCF)
A chemical company is considering a project with a lifespan of 5 years which will produce an annual inflow of £1 000. The investment outlay is £3 000 and the discount rate (interest rate)
is 10%. Should the company go ahead ?
Net Present Value = (present values) = £790
NPV is positive so go ahead with the project.
Present value = Future value x 1
( 1 + r )t
Discount
factor
Year | 0 | 1 | 2 | 3 | 4 | 5
Cash Outflow | (3 000) |  |  |  |  | 
Cash Inflow |  | 1 000 | 1 000 | 1 000 | 1 000 | 1 000
Net Cash Flow | (3 000) | 1 000 | 1 000 | 1 000 | 1 000 | 1 000
Discount factor | 1.000 | 0.909 | 0.826 | 0.751 | 0.683 | 0.621
Present Value | (3 000) | 909 | 826 | 751 | 683 | 621
DiscountCashFlow | 7
Note: brackets denote (a negative value). Cash into project is positive, Cash out of project is negative.
Note: the initial investment is made in period “0” which means that it
is not discounted (t = 0) and only future cashflows (t = >1) are discounted
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 8
Discounted Cash Flow
EXAMPLE
A company has developed a new product and has to decide whether to start full production. The marketing department has estimated that the product could sell at a price of £25 unit-1
and achieve sales of 5 000 unit a -1. Variable costs are £14 unit-1 and fixed costs £20 000 a-1. The initial investment in the production plant would be £100 000 with a residual value of £15 000 after 5 years when the product would probably be replaced.
Should full production be started?
DiscountCashFlow | 8
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 9
Discounted Cash Flow
Project: New Product Discount Rate: 10%
Net Present Value = £42 000
Year | 0 | 1 | 2 | 3 | 4 | 5
Initial Investment | (100) |  |  |  |  | 15
Fixed costs |  | (20) | (20) | (20) | (20) | (20)
Net Cash Flow | (100) | 35 | 35 | 35 | 35 | 50
Discount factor | 1.000 | 0.909 | 0.826 | 0.751 | 0.683 | 0.621
Present Value | (100) | 31.8 | 28.9 | 26.3 | 23.9 | 31.1
Variable costs |  | (70) | (70) | (70) | (70) | (70)
Sales revenue |  | 125 | 125 | 125 | 125 | 125
Sales Volume |  | 5 000 | 5 000 | 5 000 | 5 000 | 5 000
Unit price /£ |  | 25 | 25 | 25 | 25 | 25
Unit cost /£ |  | 14 | 14 | 14 | 14 | 14
£000 or £k
DiscountCashFlow | 9
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 10
Discounted Cash Flow
Graph of Cumulative Present Value for Project
Net Present Value
Cumulative Present Value / £k
Time Period
DiscountCashFlow | 10
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 11
Net Present Value
Advantages
- Includes the time value of money
- Clear choice criteria
- An absolute measure
Disadvantages
- Complex to calculate
- Difficult to relate to accounts
DiscountCashFlow | 11
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 12
Internal Rate of Return
The discount rate that makes the NPV of the investment exactly zero.
NPV = Future value
( 1 + discount rate)t
For IRR: 0 = Future value
( 1 + r )t
- calculate r
- but must solve a "t" th order polynomial equation therefore there will be multiple solutions
- can solve numerically or graphically


The Investment Decision is to accept the project proposal if
the IRR is higher than the opportunity cost of capital.
DiscountCashFlow | 12
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 13
Internal Rate of Return Example
Discount rate = 10%
Net Present Value = £790
Discount rate = 19%
Net Present Value = £58
Discount rate = 20%
Net Present Value = (£9)
Year | 0 | 1 | 2 | 3 | 4 | 5
Cash Outflow | (3 000) |  |  |  |  | 
Cash Inflow |  | 1 000 | 1 000 | 1 000 | 1 000 | 1 000
Net Cash Flow | (3 000) | 1 000 | 1 000 | 1 000 | 1 000 | 1 000
Discount factor | 1.000 | 0.909 | 0.826 | 0.751 | 0.683 | 0.621
Present Value | (3 000) | 909 | 826 | 751 | 683 | 621
Discount factor | 1.000 | 0.833 | 0.694 | 0.579 | 0.482 | 0.402
Present Value | (3 000) | 833 | 694 | 579 | 482 | 402
Discount factor | 1.000 | 0.840 | 0.706 | 0.593 | 0.499 | 0.419
Present Value | (3 000) | 840 | 760 | 593 | 498 | 419
DiscountCashFlow | 13
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 14
Internal Rate of Return
Graphical Solution of IRR
IRR
Net Present Value / £k
Discount Rate %
DiscountCashFlow | 14
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 15
Internal Rate of Return
Advantages
- Includes the time value of money
- Easy to understand figure
Disadvantages
- Relative not absolute, must be compared with a minimum required rate of return
- Multiple solutions
- Ignores risk and will favour higher risk projects
- Assumes all cash generated will be reinvested at the same rate of return
DiscountCashFlow | 15
This resource was downloaded from https://rsc.li/32MW3Gd

## Slide 16
Steps of a DCF Analysis
Establish Assessment Horizon
Estimate Relevant Cash Flows
Prepare DCF Table
Undertake NPV / IRR Analysis
Sensitivity Analysis / Scenario Analysis
DiscountCashFlow | 16
This resource was downloaded from https://rsc.li/32MW3Gd