## Slide 1
Process Capability
Whether a process is capable of meeting specification refers to the variability of the product in relation to the specification limits.
Frequency
Mean
Specification
Limits set at:
Frequency
Frequency
High
Capability
Medium
Capability
Low
Capability
ProcessCapability | 1
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>

## Slide 2
Process Capability Indices
Process Capability Index Cp
Cp = specification range
6 × standard deviation
  < 1 = low , 1.0 to 1.60 = medium , >1 = high
Process Performance Index Cpk
Cpk = lower of A or B
A = upper specification limit - long term mean
3 × standard deviation
B = long-term mean - lower specification limit
3 × standard deviation
ProcessCapability | 2
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>

## Slide 3
Calculating the Process Capability
Batch
Viscosity
Batch
Viscosity
Batch
Viscosity
Batch
Viscosity
1
169
21
167
41
167
61
169
2
165
22
163
42
163
62
163
3
169
23
167
43
169
63
167
4
163
24
160
44
166
64
162
5
169
25
166
45
170
65
171
6
163
26
165
46
162
66
164
7
165
27
170
47
170
67
168
8
160
28
162
48
161
68
165
9
167
29
169
49
170
69
168
10
161
30
163
50
163
70
162
11
168
31
169
51
166
71
171
12
163
32
162
52
162
72
162
13
166
33
170
53
171
73
168
14
162
34
160
54
165
74
163
15
167
35
169
55
167
75
171
16
161
36
164
56
164
76
164
17
167
37
170
57
169
77
168
18
165
38
163
58
164
78
164
19
168
39
168
59
168
79
168
20
161
40
162
60
163
80
166
A product has a viscosity specification of 165 +/-5 units. The data below show how the viscosity has changed over the last 80 batches. Calculate the mean and standard deviation (use a calculator) and process capability (Cp) and (Cpk) values. Is the production process high , medium or low capability? What is the consequence of the Cpk value?
ProcessCapability | 3
Notes: <number>