## Slide 1
CuSum Chart
Consider the production of batches of product with a required impurity level of 4 units. The impurity level is measured for 50 batches and
does indeed give a mean of 4 units with a standard deviation of 1.784 but was the process under control ?
Calculate the cumulative sum of the deviations from the target mean value of 4 units. Figures for the first 10 samples are given below.
Batch Number
Impurity
Deviation from target
CuSum
1
5
1
1
2
8
4
5
3
5
1
6
4
4
0
6
5
7
3
9
6
6
2
11
7
4
0
11
8
7
3
14
9
6
2
16
10
5
1
17
CuSumChart | 1
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>

## Slide 2
CuSum Charts
mean = 4
4.5
5.0
3.5
3.0
Batch number
1 5 10 15 20 25 30 35 40 45 50
10
8
6
4
2
0
25
20
15
10
5
0
-5
-10
Impurity Level
Cumulative Sum
CuSumChart | 2
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>

## Slide 3
V-masks for Mean CuSum Charts
0
1
2
3
4
5
6
7
8
9
10
Decision
interval
5
Observation number
Upper control line
(decision line)
Lower control line
(decision line)
If the CuSum plot crosses the lower control line an increase in process mean is indicated and if it crosses the upper control line a decrease in process mean is indicated
5
5
5
Batch number
1 5 10 15 20 25 30 35 40 45 50
25
20
15
10
5
0
-5
-10
Cumulative Sum
CuSumChart | 3
5
5
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>

## Slide 4
Stages in Construction of a CuSum Chart
1. Estimate the mean and standard deviation (  and  ) of the process from previous data.
Calculate the CuSum from (observations - reference value), where the reference value is
usually the mean.
3. Choose a convenient scale for the horizontal axis (sample number , days , batches)
4. Choose a vertical axis scale of approximately 2  units.
5. Plot the CuSum values. The y-axis scale may be adjusted to keep the chart on the page.
Prepare a V-mask by drawing a vertical line equal to the distance 5 on the chosen scale. Draw a horizontal line from the middle of the first vertical line back 10 scale units then draw a second vertical line equal to the distance 10centered at the end of the horizontal line.
Join up the ends of the vertical lines to produce the decision lines. Transfer this to clear film to use in real time as the data is plotted.
7. Use of the V-mask. Put the observation 0 point of the V-mask onto the latest datum point.
8. If the lower decision line crosses the CuSum plot an increase in mean is signalled. If the upper decision line crosses the CuSum plot a decrease in the mean is signalled.
CuSumChart | 4
This resource was downloaded from https://rsc.li/32MW3Gd
Notes: <number>