## Slide 1: Turning scrap metal into hi-tech steel
Read the full article at rsc.li/3oiPDZt
Ultra-low carbon steels are used in car body panels or precision alloying in automotive and electronics industries. However, much of the scrap steel being recycled is relatively high-carbon ‘hard’ steel. Conventional recycling melts scrap steel in an electric arc furnace with a reagent mixture called a slag to remove the impurities.
A new process to create ultra-pure low-carbon steel has been developed by electrochemically removing carbon from steel during recycling. By using molten slag as an electrolyte, the carbon content of molten iron was reduced from 3.78% to 0.84%. Carbon in the molten iron anode is oxidised by oxygen from silicon dioxide in the slag, producing carbon monoxide which bubbled out, with silicon ions reduced at the molybdenum cathode.
Electrolysis: an electric charge passing between an anode and cathode
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on alloys.
Image credit: © Shutterstock

## Slide 2: Turning scrap metal into hi-tech steel
What is an alloy?
Explain why alloys are harder than pure metals.
Describe the differences in properties of high-carbon and low-carbon steel.
Read the full article at rsc.li/3oiPDZt
Ultra-low carbon steels are used in car body panels or precision alloying in automotive and electronics industries. However, much of the scrap steel being recycled is relatively high-carbon ‘hard’ steel. Conventional recycling melts scrap steel in an electric arc furnace with a reagent mixture called a slag to remove the impurities.
A new process to create ultra-pure low-carbon steel has been developed by electrochemically removing carbon from steel during recycling. By using molten slag as an electrolyte, carbon content of molten iron was reduced from 3.78% to 0.84%. Carbon in the molten iron anode is oxidised by oxygen from silicon dioxide in the slag, producing carbon monoxide which bubbled out, with silicon ions reduced at the molybdenum cathode.
Electrolysis: an electric charge passing between an anode and cathode
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on alloys.
Image credit: © Shutterstock
Answers:
A mixture of different metals.
The different sizes of atoms in an alloy distort the layers in the structure, making it more difficult for them to slide over each other, so alloys are harder than pure metals.
High carbon steel is strong but brittle. Low carbon steel is softer and more easily shaped.