## Slide 1: Making hydrogen from banana peel
Researchers have devised an ultrafast biomass splitting process using light to convert dried biomass powders such as banana peel into valuable gases and solids, including hydrogen and biochar.
Banana peel contains carbon, hydrogen and oxygen in the form of carbohydrates and proteins. The banana peel is first dried to remove moisture before being ground to create a powder.
Read the full article at rsc.li/3h4im0T
From waste to fuel: could the lifecycle of the banana now include hydrogen fuel cells?
The powder is exposed to a flash of a xenon lamp. Xenon lamps produce bright white light that closely mimics sunlight, causing the powder molecules to reach a temperature of over 1000°C for a few milliseconds. The process generates 100 litres of hydrogen per kilogram of banana peel powder. The process also works with corncob, orange peel, coffee beans and coconut shell, with the potential other materials, including industrial wastes.
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on hydrogen fuel cells or sustainability.
Image credit: © Audio und werbung/Shutterstock
Answers:
Carbon, hydrogen, oxygen.
Renewable materials and waste products could be turned into a fuel. Not using fossil fuels to produce hydrogen.
The hydrogen is oxidised electrochemically to produce water and creates a potential difference.

## Slide 2: Making hydrogen from banana peel
Name three elements found in carbohydrates.
Explain why this process could be a sustainable source of hydrogen.
Hydrogen is used in fuel cells. Describe how hydrogen reacts in a fuel cell.
Researchers have devised an ultrafast biomass splitting process using light to convert dried biomass powders such as banana peel into valuable gases and solids, including hydrogen and biochar.
Banana peel contains carbon, hydrogen and oxygen in the form of carbohydrates and proteins. The banana peel is first dried to remove moisture before being ground to create a powder.
Read the full article at rsc.li/3h4im0T
From waste to fuel: could the lifecycle of the banana now include hydrogen fuel cells?
The powder is exposed to a flash of a xenon lamp. Xenon lamps produce bright white light that closely mimics sunlight, causing the powder molecules to reach a temperature of over 1000°C for a few milliseconds. The process generates 100 litres of hydrogen per kilogram of banana peel powder. The process also works with corncob, orange peel, coffee beans and coconut shell, with the potential other materials, including industrial wastes.
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on hydrogen fuel cells or sustainability.
Image credit: © Audio und werbung/Shutterstock
Answers:
Carbon, hydrogen, oxygen.
Renewable materials and waste products could be turned into a fuel. Not using fossil fuels to produce hydrogen.
The hydrogen is oxidised electrochemically to produce water and creates a potential difference.