## Slide 1: Lithium–sulfur batteries
Read the full article at rsc.li/36Q57PX
By mixing sulfur into carbon nanofibers the sulfur forms a rare rectangular prism structure made of eight sulfur atoms instead of the normal crown structure. This rectangular prism structure stops the formation of polysulfides completely. Instead, lithium sulfide forms directly, allowing the battery to work unimpeded.
Sulfur is cheap, abundant, and has a low density which could lead to lithium–sulfur batteries having advantages especially for applications where energy density is critical – like aviation.
The wanted reaction at a Li–S battery cathode is for the positive lithium ions to react with sulfur to make lithium sulfide. With existing battery electrolytes unwanted polysulfides also form, which react with the electrolyte and kill the cell.
Next generation energy storage is driving the automotive industry forward
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on cells and batteries.
Image credit: © Getty Images

## Slide 2: Lithium–sulfur batteries
What is the name for different structures of the same element?
Explain what happens to the reactions in a cell when a cell is recharged.
Suggest why a Li–S battery could have advantages for use in aviation.
Read the full article at rsc.li/36Q57PX
By mixing sulfur into carbon nanofibers the sulfur forms a rare rectangular prism structure made of eight sulfur atoms instead of the normal crown structure. This rectangular prism structure stops the formation of polysulfides completely. Instead, lithium sulfide forms directly, allowing the battery to work unimpeded.
Sulfur is cheap, abundant, and has a low density which could lead to lithium–sulfur batteries having advantages especially for applications where energy density is critical – like aviation.
The wanted reaction at a Li–S battery cathode is for the positive lithium ions to react with sulfur to make lithium sulfide. With existing battery electrolytes unwanted polysulfides also form, which react with the electrolyte and kill the cell.
Next generation energy storage is driving the automotive industry forward
Notes: This slide summarises a recent article published by Chemistry World. Use this slide as a lesson starter for a lesson (14–16) on cells and batteries.
Answers:
Allotrope.
The chemical reactions are reversed.
Li–S battery would have a low density and so would be advantageous for aviation where cells need to be lightweight. Sulfur is abundant unlike alternatives such as cobalt.
Image credit: © Getty Images