## Slide 1: 14–16 years
Phytomining
https://rsc.li/3xDGktk

## Slide 2: You should be able to:
Learning objectives
Use key words associated with phytomining.
Sequence the processes involved in phytomining.
State an advantage and disadvantage of phytomining.
Describe how plants can be used to extract metals from low grade ores.

## Slide 3: Metals
Introduction
Metals are very valuable, especially for technology such as mobile phones. However, there is only a finite resource of metal compounds to extract from the Earth.
What is a finite resource?
Notes: Image © Shutterstock

## Slide 4: Mining to extract metals
Information
Rock containing a lot of valuable mineral or metal compound is called a high grade ore.
Traditional methods of extracting it from the ground involve mining: digging, moving and disposing of large amounts of rock.
This leaves behind polluted ground.
Notes: Image © Shutterstock

## Slide 5: Low grade ore
Information
When the concentration of valuable mineral in the rock diminshes it is no longer economically viable to dig it up and extract the metal from it.
Rock with a low concentration of a valuable metal compound (mineral) is called a low grade ore.

## Slide 6: Phytomining (slide 1 of 2)
Information
When there is only a small concentration of valuable mineral in a low-grade ore, then a process called phytomining, involving growing plants, is economic to use.
phyto = relating to plants
mining = to dig or tunnel

## Slide 7: Phytomining (slide 2 of 2)
Information
Plants called hyperaccumulators are grown in what is often contaminated soil. They absorb the minerals in the low-grade ore via their roots and what they don't use is stored and concentrated in their leaves.
hyper = over, above, beyond
accumulate = gather or collect

## Slide 8: Extracting the mineral from the plant
Information
When the plants have grown enough, they are burnt in air and the impure metal compound is found concentrated in the ash.

## Slide 9: Purifying the metal
Information
The ash can be reacted with acid to produce a copper compound electrolyte for electrolysis.
Or a displacement reaction using scrap iron can be used to then purify the metal from the ash.
Why does iron displace copper?

## Slide 10: Electrolysis
Retrieval questions
Write a word equation for the reaction between copper oxide and sulfuric acid.
Does the copper form on the anode or cathode?
Give the electrode equation.

## Slide 11: Advantages of phytomining (compared to traditional mining)
Advantages
Can extract valuable metals from low grade ores when it is not usually economic to do so.
Requires less energy than traditional mining.
Produces less air pollution*.
It can be used to clean contaminated soil and regenerate the land from closed down mines.
*This process still gives out CO2 as you burn the plants but you may consider it as carbon neutral as you give out the CO2 that the plant took in.

## Slide 12: Disadvantages of phytomining (compared to traditional mining)
Disadvantages
It is a slower process as you need to wait for the plants to grow.
You need access to the correct plants and conditions to grow things on the contaminated soil*.
*As the land is often contaminated you are not usually using land that could otherwise be used for food.

## Slide 13: Test your learning
Activities
Now have a go at the following activities:
Phytomining cloze
Phytomining sequencing activity
Phytomining storyboard
Notes: Student activities available from: https://rsc.li/3xDGktk