## Slide 1: Emulsifiers
Download the teacher notes, student workbook and technician notes that accompany this resource at rsc.li/3cpvP4k.

## Slide 2: Learning objectives
By the end of this session, you will be able to:
Explain how soap acts as an emulsifier in cleaning.
Explain how emulsifiers are used to make hand creams.

## Slide 3: What is soap?
Soap is made from fats and alkaline solutions (known as lye).
When fats and alkalis mix, a chemical process occurs called saponification.
The resulting substance is soap.
Everything else is just added scent and colouring.
Soaps have been used and developed since the ancient Roman times.
Introduction
Notes: © New Africa/Shutterstock
© rawf8/Shutterstock

## Slide 4: Senior scientist, household goods
Meet Phillip, a senior scientist, who leads a team of researchers working on ways to improve the quality and performance of household products such as soaps and shampoos.
Career link
Senior scientist
Notes: Read the profile at https://edu.rsc.org/job-profiles/senior-scientist-household-goods/4010860.article (accessed 11 April 2023).

## Slide 5: Demonstration: why does soap clean?
While watching the demonstration, record your observations in your student workbook.
Think about the behaviour of the oil and water and how it may change when the washing up liquid is added.
Notes: Use the next two slides to go through the learners’ observations and answers to the questions in the student workbook.

## Slide 6: Demonstration: why does soap clean?
1. (a) The oil and water do not mix. The oil forms an upper layer on top of the coloured water.
  (b) The oil and water do not mix. The oil is less dense than water so will float on top of the water.
2. (a) When the washing up liquid was added, the oil and water were able to mix together.
  (b) The washing up liquid allows the water and oil to mix by acting as an emulsifier. An emulsion is formed, where the oil is dispersed as small droplets throughout the water.
Answers

## Slide 7: Demonstration: why does soap clean?
3. An emulsion is formed when one liquid is dispersed through another liquid in the form of small droplets.
4. An emulsifier is an agent which allows two liquids to mix to form an emulsion.
Answers

## Slide 8: Removing grease and dirt
The washing up liquid (soap) molecules arrange themselves so the oil and water can mix.
The washing up liquid molecules each have a hydrophilic (water-loving) head and a hydrophobic (water-hating) tail.
The detergent molecules’ hydrophobic tails attach to the oil and the hydrophilic heads stick out into the water.
This forms a droplet of oil which is suspended in the water.
Notes: © adapted from Atallah Salmeh/Shutterstock
Link this to the use of washing up liquids and soaps for cleaning. Tell learners: soap cleans by removing grease and dirt off your body or clothes because the suspended oil drops bond to the dirt and can be washed away.

## Slide 9: Consumer products technician
Meet Robert, a consumer products technician, who develops materials which can improve the properties of household products such as washing up liquids and soaps.
Career link
Consumer products technician
Notes: Watch the video at https://edu.rsc.org/job-profiles/consumer-products-technician/4010850.article (accessed 11 April 2023).
Video length: 3:47

## Slide 10: Making hand cream
Activity 1
See student workbook

## Slide 11: What are hand creams?
Hand creams are used to moisturise and soften the skin.
Hand creams are emulsions. They contain oil, water and an emulsifier, along with any other ingredients to add scent or moisture.
Activity 1

## Slide 12: Making hand cream
1. Place 4 g of petroleum jelly and 4 g of coconut oil into a 250 ml beaker and warm in a hot water bath until they melt and turn to liquid.
2. Measure 40 ml of lecithin solution into a second beaker and place it in the hot water bath.
3. When the oils have fully melted, remove both beakers from the water bath. Take care when removing the beaker from the water bath as it may be hot.
4. Slowly add the melted oils to the warm lecithin solution while constantly stirring.
Activity 1

## Slide 13: Making hand cream (continued)
5. Once all the oil has been added, a cream should start to form.
6. Add a drop or two of an essential oil with a scent of your choice.
7. Cool the mixture down in a cold-water bath.
Once cooled, use the spatula to scoop your hand cream into the sample vial provided.
Answer
(a) Lecithin is the emulsifier, which allows the oil and water to mix to make a cream.
Activity 1

## Slide 14: Analysing hand cream using a microscope
Activity 2
See student workbook

## Slide 15: Analysing hand cream using a microscope
In this activity you will use a microscope to look at the sample of hand cream you made in greater detail.
1. Place a drop of your hand cream on the microscope slide from the sample vial and carefully cover with a glass cover slip. Take care when handling the slide and cover slip.
2. Rotate the microscope’s objective lenses so that the lowest power objective lens is above the stage.
3. Place the slide on the microscope stage and make sure the sample is in the middle. Secure the slide with the clips.
Activity 2
Notes: Tell learners : In this activity you will use a microscope to look at the sample of hand cream you made in greater detail. If you look at the hand cream with the naked eye, you will not be able to see the individual droplets of oil very clearly, but using the microscope means that you should be able to see how the oil droplets are spread throughout the mixture.
In case learners have not used a microscope recently, provide the following advice to help them out:
If you cannot see the sample clearly, turn up the light.
When focusing, raise the stage until it is as high as it will go, then lower it slowly using the coarse focus. That way there is less risk of breaking the slide.
Make sure you are focused on the lowest setting (usually ×10) before increasing to ×40. It will then be easier to focus on high power as it should be close to the optimum focus already.

## Slide 16: Analysing hand cream using a microscope (continued)
4. Adjust the height of the stage using the coarse focus dial.
5. Look down the eyepiece.
6. Increase the magnification by rotating the objective lenses to the next highest power and use the fine focus dial to bring the sample back into focus.
Draw what you see.
  Answer
(b) Hand cream is an emulsion as it is made up of oil droplets suspended in a watery solution.
Activity 2
Notes: Learners should be able to see oil droplets suspended in the watery solution forming an emulsion
Answers to (a) is learner dependent. Their drawing should show what they see when they look at their hand cream sample, including oil and water labels.

## Slide 17: Acknowledgements
This resource was originally amended and adapted by the University of Reading to support outreach work delivered as part of the Chemistry for All project.
To find out more about the project, and get more resources to help widen participation, visit our Outreach resources hub: rsc.li/3CJX7M3.
Unless explicitly stated, all images are © Royal Society of Chemistry.
The Royal Society of Chemistry gratefully acknowledges the permissions granted to reproduce copyright material in this resource. Every effort has been made to contact the holders of copyright material, but if any have been inadvertently overlooked, the Royal Society of Chemistry will be pleased to make the necessary arrangements at the first opportunity.