## Slide 1: Recycling wind turbine blades
Science research news
Slide by Neil Goalby. Available from rsc.li/3p7xcLE
Wind turbine blades are made by bonding carbon fibre meshes with a thermosetting epoxy polymer to form a composite. Cross links in the polymer make the composites strong, but it also means that they can’t be melted. This makes them unrecyclable and they often end up in landfills.
Researchers have added pieces of epoxy composite into a mixture of solvents, along with a ruthenium catalyst and heated the mixture to 160°C for three days. This method breaks a specific C–O bond in the resin, which splits up the polymer into its original building blocks so that it can be reused.
Decommissioning our wind turbines will require a lot of recycling
Questions
Describe why material making wind turbine blades is called a composite material. Describe the structure of a thermosetting polymer. Explain why thermosetting polymers are difficult to recycle.
© Veni/Getty Images
Notes: This slide summarises a recent article published by Chemistry World. Use this as a lesson starter when teaching composite materials and thermosetting polymers.
Answers
The material used to make wind turbine blades is made of carbon fibres bound together by an epoxy resin matrix.
Polymer chains are linked to each other by strong cross-links.
The strong cross-links mean the polymer cannot be melted down. This makes recycling difficult.