## Slide 1: 11–14 years
Fight fire!
Fill up with foam

## Slide 2: Learning objectives
Plan an investigation to identify the reagent that produces the largest quantity of carbon dioxide foam.
Record the investigation results and make a conclusion.
Design a ‘foam launcher’ suitable for delivering the foam to a fire.

## Slide 3: Introduction
Three things are needed for fire:
  heat
  fuel
  oxygen
By removing any one of these a fire can be extinguished.
Introduction
Notes: Image adapted from: © Fihusainh/Shutterstock

## Slide 4: Fire extinguishers
Carbon dioxide is widely used in fire extinguishers.
Because it is denser than air, it smothers and extinguishes fires by preventing further oxygen from reaching the source of the flames.
Introduction
Notes: Image: © Daniel Heighton/Shutterstock

## Slide 5: Controlling fires
One of the difficulties with putting out big fires in the open air is that the wind blows away the carbon dioxide gas, allowing more oxygen to reach the fire and keeping it burning.
Therefore, ideally, we should apply carbon dioxide as a blanket of thick foam, not a gas.
Introduction
Notes: Image: © AVN Photo Lab/Shutterstock

## Slide 6: Your task: stage 1
Your task is to investigate which extra reagent produces the largest quantity of carbon dioxide foam.
Your first two reagents will be:
Sodium hydrogen carbonate (6 spatulas)
Sulfuric acid, 1.4 mol dm-3 (20 cm3) (WARNING: irritant to eyes and skin)
The sodium hydrogen carbonate and acid react together to produce carbon dioxide gas.
Your task
Sodium hydrogen carbonate + acid  salt + water + carbon dioxide

## Slide 7: Your task: stage 2
Then, you must investigate which one extra reagent produces the largest quantity of foam. The reagents to investigate are:
Washing detergent powder (6 spatulas) (WARNING: irritant to eyes and skin)
Washing up liquid solution (20 cm3)
Water (20 cm3)
Key questions to consider:
In what order will you add the reagents?
How are you going to measure the quantity of foam produced?
Your task

## Slide 8: Method
Plan an investigation to identify the extra reagent that produces the largest quantity of carbon dioxide foam.
Your plan must include:
• The reagents used and their quantities.
• The order in which the reagents will be added.
• What you will measure.
• What safety precautions you will take to avoid eye and skin contact.
Results table
Draw a suitable table to record your results. Include quantities for the reagents used, along with units for all measurements.
Conclusion
Based on your results, identify the extra reagent that produced the largest quantity of carbon dioxide foam.
Your task

## Slide 9: Question 1
Questions
1. This question is about carbon dioxide and how it can be produced.
(a) Carbon dioxide is a compound made up of one carbon atom and two oxygen atoms. Which option shows the formula for carbon dioxide written correctly?
A. CO2 B. CO2 C. C2O D. CO2
(b) Carbon dioxide is produced from the reaction of an acid and a metal hydrogen carbonate. A salt and water are also produced. Write a word equation to represent this reaction.
(c) Which test can be used to prove that the gas produced is carbon dioxide?
A. Damp litmus paper is bleached.
B. A glowing splint relights.
C. Limewater turns cloudy when the gas is bubbled through it.
D. A lit splint burns with a squeaky pop.

## Slide 10: Question 2
2. Carbon dioxide extinguishes fires by preventing oxygen from reaching the source of the flames. Oxygen is one of three essential things needed for combustion.
(a) Complete the fire triangle to show the three things needed for combustion.
(b) For each of the methods below, identify which of the three components of the fire triangle is removed. For example, switching off the gas supply to a gas fire removes the fuel.
i. A forest fire extinguished using water.
ii. Chopping down trees to create a fire break in a woodland fire.
iii. A chip pan fire extinguished by placing a fire blanket over the pan.
Questions

## Slide 11: Challenge: ‘foam launcher’
Once you have determined the best combination of reagents, design a ‘foam launcher’ that could be used to safely deliver the foam to put out a fire.
Key questions to consider:
How can the foam be safely directed at the fire?
Do you want the foam to be stored or formed ‘on demand’?
Challenge

## Slide 12: Challenge: pitch your launcher
Prepare a pitch to promote your foam launcher to a panel of industry experts.
Top tips for success:
Have a clear, compelling opening that introduces your product.
Briefly explain your design and the reason behind some of the key design features.
Prove it will work!
Explain why you, and your foam launcher are the best on the market.
Challenge