## Slide 1: 14–16 years
Life cycle assessment: shopping bags

## Slide 2: Learning objectives
Understand how the overall environmental impact of a product is assessed using a life cycle assessment.
Evaluate the use of three different types of shopping bag using a life cycle assessment of each one.

## Slide 3: The problem
In 2008, supermarkets in the UK gave away approximately 10 billion lightweight single-use carrier bags. This is around 10 bags a week per household.*
Under pressure from the public, the media and their commitment to environmental policy the government needed to act on single-use plastic.
The Environment Agency stepped up to assess the environmental impact of lightweight single-use carrier bags against other alternatives.
Their findings informed the government’s plan to tackle plastic waste.
Introduction
© Shutterstock
Notes: * Figures from DEFRA 2009 – see slide 21 for full reference

## Slide 4: Finding data
A study was commissioned by the Environment Agency (EA) to assess the life cycle environmental impacts of different supermarket carrier bags available in the UK in 2006. The report was completed and published in 2011.
This type of study is called a Life cycle assessment or LCA. The target audience for this report was outlined as:
supermarkets, other retailers, environmental organisations and consumers
public authorities, eg the Department for Environment, Food and Rural Affairs (DEFRA).
Introduction
Notes: See slide 21 for the full reference and link to report.

## Slide 5: What is a life cycle assessment?
A life cycle assessment looks at every stage of a product’s life and assesses the impact it has on the environment during each stage.
Five main stages are analysed during a life cycle assessment:
Obtaining the raw materials
Manufacturing and processing
Transport (at all stages)
Consumer use
Disposal
Introduction

## Slide 6: Your task
1. Use the student sheet to complete a life cycle assessment for three different types of supermarket carrier bag:
Single-use plastic bag
Reusable plastic bag
Cotton bag
Use the information on these slides or research on the internet, plus your own subject knowledge.
Introduction
2. Make a recommendation to the Department for Food and Rural Affairs (DEFRA) based on your assessment.

## Slide 7: Bag 1: single-use plastic bag
Raw materials
The EA life cycle assessment describes this bag type as: Conventional high-density poly(ethene) (HDPE) bags
This is the lightweight, plastic, carrier bag used in almost all UK supermarkets [in 2006] and often provided free of charge … It has been termed ‘disposable’ and ‘single use’.
The raw material for a single-use bag is a polymer made from crude oil.
Fractional distillation and cracking are used to obtain ethene from the crude oil. This is then polymerised under carefully controlled conditions to form HDPE.
© Shutterstock
Mass of raw material to make one bag = 8.12 g

## Slide 8: Bag 2: reusable plastic bag
Raw materials
The EA life cycle assessment describes this bag type as:
Low-density poly(ethene) (LDPE) bags
These are heavy duty plastic bags, commonly known as ‘bags for life’ and are available in most UK supermarkets. The initial bag must be purchased from the retailer but can be replaced free of charge when returned. The old bags are recycled by the retailer. The raw material for a reusable bag is a polymer made from crude oil.
Fractional distillation and cracking are used to obtain ethene from the crude oil. This is then polymerised under carefully controlled conditions to form LDPE.
© Shutterstock
Mass of raw material to make one bag = 34.94 g

## Slide 9: Bag 3: cotton bag
Raw materials
The EA life cycle assessment describes this bag type as:
This type of bag is woven from cotton, often calico, an unbleached cotton with less processing, and is designed to be reused many times. The raw material for the bag is cotton from the cotton plant. The processes involved in growing cotton include soil cultivation, fertilisation, application of pesticides, irrigation, harvesting and ginning (where the cotton is dried and cleaned in a factory).
© Shutterstock
Mass of raw material to make one bag = 183.11 g

## Slide 10: Energy consumption and waste generation
Manufacturing and processing
All plastic bags are produced from plastic melt. This is generally blown and sealed to form a bag. The energy demand for these processes in mainly met by grid electricity and this energy consumption depends on the polymer type, density, production equipment and capacity.
The processing involved in turning cotton into cotton bags includes yarn production, textile refinement and weaving.
The energy consumption and waste (mass of material not converted into the end-product*) generated by the production of 1000 bags is shown in the table.
Bag type | Electricity (kWh kg-1) | Waste (g)
Single-use plastic bag | 0.758 | 418.4
Reusable plastic bag | 0.932 | 171.2
Cotton bag | 0.06 | 1,800
Notes: *A thorough explanation of this term is not provided in the EA report, however, this is our understanding of the meaning of the term ‘waste’ in this context.

## Slide 11: The transport scenarios for carrier bags
Transport
Bag type | From | To | Transport modes | Distance
Single-use plastic bag | Polymer resin* producer in China/ Indonesia/Malaysia | Bag producer in China/ Indonesia/Malaysia | Lorry Sea freight | 100 km 500 km
 | Bag producer in China/ Indonesia/Malaysia | Bag importer in UK | Lorry Sea freight Rail | 100 km 15,000 km 280 km
 | Bag importer | Supermarket | Lorry | 200 km
Reusable plastic bag | Polymer resin producer in Europe | Bag producer in Turkey** | Lorry | 300 km
 | Bag producer in Turkey | Bag importer in UK | Sea freight Rail | 5,000 km 280 km
 | Bag importer | Supermarket | Lorry | 200 km
Cotton bag | Textile producer in China | Bag producer in China | Lorry | 100 km
 | Bag producer in China | Bag importer in UK | Lorry Sea freight Lorry | 100 km 15,000 km 280 km
 | Bag importer | Supermarket | Lorry | 200 km
Notes: *Transport of titanium oxide and chalk to the bag manufacturer are also included in the Environment Agency LCA report. However, the numbers were missing for bags produced in Turkey so we have left them out here for a more direct comparison. **90% of LDPE bags were produced in Turkey at the time of the Environment Agency LCA report in 2006. The other 10% were produced in Asia (China, Indonesia and Malaysia).

## Slide 12: Global warming potential
Environmental impact
Global warming potential is a measure of how much the greenhouse gas emissions in a particular process are estimated to contribute to global warming.
It is measured in CO2 equivalents: all the different greenhouse gas emissions are converted to the amount of CO2 that would cause the same amount of warming. This way, global warming potential can be expressed as a single number.
Bag type | Global warming potential (kg CO2 equivalents)
Single-use plastic bag | 1.578
Reusable plastic bag | 6.924 (no reuse) 1.385 (used 5 times)
Cotton bag | 271.533 (no reuse) 1.570 (used 173 times)
Exact percentages vary for each bag, but the most emissions are caused by the extraction and production of the raw materials. Manufacturing and processing are next, then transport, then disposal.
See next slide

## Slide 13: Primary and secondary consumer use
Consumer use
The table below shows the number of times you need to use reusable bags (plastic or cotton) to take them below the global warming potential of single-use bags.
If any type of bag is used again it further reduces its environmental impact.
 | Number of times bag needs to be used to match global warming potential |  |  | 
 | Single-use bag (no reuse) | Single-use bag (40.3% reused as bin liners) | Single-use bag (100% reused as bin liners) | Single-use bag (used 3 times)
Reusable plastic bag | 4 | 5 | 9 | 12
Cotton bag | 131 | 173 | 327 | 393

## Slide 14: Testing to destruction
Consumer use: the experiment
The EA study used expanded polystyrene beads to measure the volume of the bags by filling each bag to capacity (up to the handles).
They then used a jog testing machine to simulate walking with a bag containing a 5 kg load for 4 minutes before adding an additional 1 kg every minute until the bag failed.
The study found that an average single-use bag had a capacity of 18.22 kg and lasted for 17 minutes and 32 seconds. The average reusable bag had a capacity of 19 kg and lasted 18 minutes and 30 seconds.
© Shutterstock

## Slide 15: Ensuring a fair comparison
Consumer use
The weight, volume, quality and capacity of the bags assessed in the study is not the same. The EA needed to adjust the number of bags compared so that the LCA was fair. They used the average volume and the average weight each type of bag can carry (see previous slide), to calculate the average number of items that each bag can carry.
They used this to work out the total number of bags need to carry a month’s shopping (found to be 483 items on average).
 | Average volume per bag (litres) | Average number of items per bag | Number of bags needed per month for average shopper
Single-use plastic bag | 19.10 | 5.88 | 82.14
Reusable plastic bag | 21.52 | 7.96 | 60.68
Cotton bag | 28.65 | 10.59 | 45.59

## Slide 16: Reuse of single-use plastic carrier bags
Consumer use
A study of lightweight carrier bag usage (Waste and Resources Action Programme, 2005) found that 59 percent of respondents reused all carrier bags, 16 percent reused most of them, 7 percent reused around half and 7 percent reused some of them.
Reuse applications* | Percentage of respondents that reuse single-use carrier bags in each application
Use as a bin liner in kitchen | 53
Use as a bin liner in other rooms | 26
Put rubbish into it then throw it away | 43
For dog/cat/pet mess | 11
Reuse for supermarket shopping | 8
Reuse for other shopping | 10
To store things in at home | 14
For packed lunches | 8
Do not have a use/discard | 11
Notes: *Other reuse applications not included in the table (because their percentage was below 5%) are: Garden refuse (1%), Carry other things when going out (4%), Put football/Wellington boots in (1%), Give to charity shops (1%), Keep bottles/cans in for recycling (1%), Other uses (2%).
Full reference and link to the study can be found on slide 21.

## Slide 17: End-of-life processes
Disposal
The following options were considered for each bag in the analysis. The recycling of cotton bags was not included as no evidence was found to support this as a realistic option.
Can you think of any other options for the disposal of these items?
Bag type | Landfill | Incineration | Mechanical recycling
Single-use plastic bag |  |  | 
Reusable plastic bag |  |  | 
Cotton bag |  |  | 

## Slide 18: Conclusion
Which of the bags do you think has the least environmental impact?
Suggest an action for the government to reduce the impact of shopping bags on the environment. Use evidence from your completed LCA to support your recommendation.
Conclusion
Notes: Student sheet and teacher answers available from https://rsc.li/3HPZ78N

## Slide 19: The carrier bag charge
In October 2015, the 5p carrier bag charge was introduced in England for single-use carrier bags in supermarkets. This was increased to 10p and extended to other retailers in May 2021. Similar charges are also in place across Scotland, Wales and Northern Ireland.
DEFRA reports that, since the introduction of the single-use carrier bag charge, the number of single-use plastic bags used in supermarkets in England has gone down by more than 95%.
The charge is not a tax. Supermarkets and retailers are encouraged to donate the money to good causes.
Do you think this was a successful scheme?
What might you have done differently?
Conclusion
Notes: Student sheet and teacher answers available from https://rsc.li/3HPZ78N

## Slide 20: What’s next?
Did you find it easy to judge which bag had the most impact on the environment? Could you easily compare the bags, or did you have to make some assumptions or judgements based on data you didn’t have?
How could you extend this study to include other packaging? Think about how you would assess paper bags or packaging for clothes, online purchases or takeaway food.
Conclusion

## Slide 21: References
Carrier bags: why there’s a charge, Department for Environment, Food and Rural Affairs Policy paper, Updated 21 May 2021 https://www.gov.uk/government/publications/single-use-plastic-carrier-bags-why-were-introducing-the-charge/carrier-bags-why-theres-a-5p-charge [Accessed: 08.01.2024]
Life cycle assessment of supermarket carrier bags: a review of the bags available in 2006, Environment Agency, Published February 2011 https://www.gov.uk/government/publications/life-cycle-assessment-of-supermarket-carrierbags-a-review-of-the-bags-available-in-2006 [Accessed 08.01.2024]
Carrier Bag Usage And Attitudes Benchmark and Target Market Study Research Findings, WRAP (Waste and Resources Action Programme), Published March 2005 https://www.scribd.com/document/121801888/Carrier-Bag-Usage-2005 [Accessed 08.01.2024]
References